# netsh
- Netsh Technical Reference|
- Netsh commands for Interface Internet Protocol version 4 (IPv4)
- https://michlstechblog.info/blog/windows-show-and-configure-network-settings-using-netsh/
## DHCP használata
netsh interface ip set address name="LAN" source=dhcp netsh interface ip set dns name="LAN" source=dhcp

## Statikus hálózati beállítás
### Router nélkül
netsh interface ip set address name="LAN" source=static addr=192.168.0.10 mask=255.255.255.0 gateway=none netsh interface ip set dns name="LAN" source=none

### Routerrel
netsh interface ip set address name="LAN" source=static addr=192.168.0.10 mask=255.255.255.0 gateway=192.168.0.1 netsh interface ip set dns name="LAN" source=static addr=192.168.0.1 register=none validate=no

### Routerrel és 2 külső DNS szerverrel
netsh interface ip set address name="LAN" source=static addr=192.168.0.10 mask=255.255.255.0 gateway=192.168.0.1 netsh interface ip set dns name="LAN" source=static addr=8.8.8.8 register=none validate=no netsh interface ip add dns name="LAN" addr=8.8.4.4 index=2 validate=no

## Fájlmegosztás engedélyezése
https://websiteforstudents.com/share-files-on-ubuntu-16-04-lts-with-windows-10-systems/
netsh advfirewall firewall set rule group="File and Printer Sharing" new enable=Yes netsh advfirewall firewall set rule group="Network Discovery" new enable=Yes